Band saw

Rules for use:

- Always wear safety glasses and hearing protection

- Do not operate while wearing jewelry or loose long sleeves or hair

- Always keep hands away from the blade

- Never cut with any part of your body in the path of the blade

- Keep your eyes on the blade at all times while in use

- Use only when a Technical Director is present

- Never use without permission of a Technical Director

Procedures for use:

- Make certain the blade is correct. For curves you want a thin blade, for straight lines you want a thick blade

- Turn on the air handler and open the vent

- Place your material on the saw table next to the blade

- Adjust the guard over the blade so it ends approximately ¼” above the material

- Set your work on the saw table, approximately ½” from the blade

- Turn on the saw

- Slowly feed the material through the blade keeping your fingers out of the path of the blade. Hold the material securely so your hands do not slip. Sometimes it is easier to hold the material behind the blade with your right hand

- When you are finished cutting, turn off the saw

Remember, if you don’t feel comfortable with something – DON’T DO IT!

The Band Saw is not a toy. Treat it with respect.

This student has been trained in the proper use of the Band Saw.

Tech Director_________________________________________________

Date______/______/______

I understand the above rules, and will follow them at all times.

Student’s Signature____________________________________________

Date______/______/______