Impact Driver

Rules for use:

- Always wear safety glasses and hearing protection

- Do not operate while wearing jewelry or loose long sleeves or hair

- Always keep hands away from the screw and bit

- Keep your eyes on your work at all times while in use

Procedures for use:

- Check the bit. If it is chipped or worn, see the Tech Director for a new one. On the collar make sure the arrow is pointing toward the drill bit

- Chuck the screw bit. Remove the bit that is in the drill by pulling forward on the collar, insert the bit, release the collar.

- Put the drill in forward gear. There is a button on the handle, if the arrow is pointed toward bit then you are going forwards.

- Place a screw on the bit. It should fit snugly. If it does not, check the screw head for obstructions. Discard screws that are damaged

- Place the screw onto the wood

- Move your hand from the screw onto the back of the screw gun

- Slowly squeeze the trigger. The guns are variable speed, so the more you pull the trigger, the faster they spin. It spins VERY fast until it catches in the wood.

- Start slowly. Once the screw catches and starts going into the wood, the driver will slow down and make a loud noise. Lean into the drill, using your body weight to help drive the screw into the wood

- Sink the screw so that the head is slightly below the level of the wood. It is easy to over countersink screws with the impact driver which makes strike difficult.

- If you feel the drill bouncing in and out of the screw head stop immediately; continuing will strip the head and make it difficult to continue or remove the screw. Set the gun in reverse by pushing the button on the handle all the way to the right and slowly back the screw out ½” or so. Put the gun back into forward and begin again

Remember, if you don’t feel comfortable with something – DON’T DO IT!

The Screw Gun is not a toy. Treat it with respect.

This student has been trained in the proper use of the Screw Gun.

Tech Director_________________________________________________

Date______/______/______

I understand the above rules, and will follow them at all times.

Student’s Signature____________________________________________

Date______/______/______