Panel Saw

Rules for use:

- Always wear safety glasses and hearing protection

- Do not operate while wearing jewelry or loose long sleeves or hair

- Always keep hands well clear of the saw carriage

- Rotate the saw carriage so that the saw trigger faces the wood

- Always rip from right to left and crosscut from top to bottom

- Never use without permission of a Technical Director

Procedures for use:

- Turn on the air handler and open the vent for the panel saw

- Rotate the saw to the correct plane – up and down for crosscutting, right to left for ripping

- Make sure the saw is pointed in the right direction

# To crosscut –

  - Set the stop at the correct distance using the guide

  - Insert the wood into the panel saw, making sure it butts snugly against the stop and rear supports. One person should hold it tightly in place

  - Pull and lock the trigger

  - Slowly move the saw down through the wood until you reach the bottom. Only hold the saw by the handle and keep hands, feet, etc. out of the path of the saw

  - Release the trigger by pulling and letting it go

  - When the saw blade has stopped moving, bring the saw back to its starting position

  - Remove the pieces of wood

# To rip –

  - One person should be on each side of the saw. One person is the ripper, one is the receiver

  - Set the carriage at the correct height, using the guide. Make sure the crosscut stop isn’t in the way

  - Pull and lock the trigger

  - The ripper should slowly push the wood through the saw. You should push with a slight downward pressure.

  - When the ripper’s hands near the saw carriage, he or she should tell the receiver to start pulling the wood. As the receiver starts gently pulling, the ripper should release the wood

  - When the wood is all the way through the saw, release the trigger by pulling and letting it go

Remember, if you don’t feel comfortable with something – DON’T DO IT!

The Panel Saw is not a toy. Treat it with respect.

This student has been trained in the proper use of the Panel Saw.

Tech Director_________________________________________________

Date______/______/______

I understand the above rules, and will follow them at all times.

Student’s Signature____________________________________________

Date______/______/______

I understand my child has been properly trained on the use of the Panel Saw, and give my permission for him/her to use it under the above conditions.

Parent’s Signature____________________________________________

Date______/______/______