Pneumatic Stapler

Rules for use:

- Always wear safety glasses and hearing protection

- Do not operate while wearing jewelry or loose long sleeves or hair

- Always keep hands well clear of the staple path

- Keep your eyes on your work at all times

- Never point the stapler at anyone

- Do not pull the trigger unless you are stapling

Procedures for use:

- Plug in and turn on the compressor

- Set the air pressure to 80lb, unless instructed otherwise

- Load the staple gun with the correct size staple. The Technical Director will tell you which staples to use, how to load the particular stapler, and how to oil it if it needs oiling

- Make sure the stapler is set for single shot

- Plug the air hose into the stapler and compressor

- Test fit your pieces to make sure they fit

- Glue the wood (in certain instances this step may be skipped. Your Tech Director will let you know)

- One person should hold the joint in alignment, making sure surfaces that need to be flush are

- Make sure that all hands are further away from the stapling area than the length of the staple. This applies in ALL directions; staples may enter the wood, hit an obstruction, and come out in any direction, even backwards

- Press the stapler against the wood. New Trier staplers have safeties, so they should not fire unless they are pressed firmly against something

- Line the stapler up, so that the staple is going into the middle of the wood. Keep the stapler level, so the staple does not go in at an angle and come out of the side of the wood

- Pull the trigger while pressing the stapler into the wood. Do not let the recoil push the stapler back

- Check that the staple is not coming out of the wood. If it is, clip the end off with side cutters and pound the ends into the wood

- Clean up any glue drips or overflow

Remember, if you don’t feel comfortable with something – DON’T DO IT!

The Pneumatic Stapler is not a toy. Treat it with respect.

This student has been trained in the proper use of the Pneumatic Stapler.

Tech Director_________________________________________________

Date______/______/______

I understand the above rules, and will follow them at all times.

Student’s Signature____________________________________________

Date______/______/______

I understand my child has been properly trained on the use of the Pneumatic Stapler, and give my permission for him/her to use it under the above conditions.

Parent’s Signature____________________________________________

Date______/______/______